## Slide 1: KneeGait-Edge
Democratizing Gait Intelligence
A ₹516 edge-AI wearable for accessible gait analysis
GRAVITON (CGC University Mohali)
Team Astronauts
Rahul Bansal (CTU)
Prateek Dhar Dwivedi (NIELIT Deemed to be University Ropar)
Saksham Verma (NIELIT Deemed to be University Ropar)
Krishna Kumar (NIELIT Deemed to be University Ropar)
Notes: KneeGait-Edge is a low-cost wearable that brings gait screening out of the lab. One shank-mounted IMU, an ESP32 doing the processing and the machine learning on-device, and a browser dashboard over Bluetooth. Prototype cost: about ₹516.

## Slide 2: Gait analysis is locked behind labs
THE ACCESS GAP
Traditional approach
Specialized equipment
Expensive infrastructure
Laboratory-dependent
Limited access
650M+
adults live with knee osteoarthritis worldwide
$20K–$50K
optical motion-capture systems (Vicon, Qualisys)
₹516
our single-IMU edge-AI prototype
Can gait intelligence become portable, accessible and affordable?
The need: Portable • Affordable • Real-time • Accessible
Notes: Optical motion capture costs tens of thousands of dollars and lives in a lab. Knee osteoarthritis affects over 650 million adults, so the gap between who needs gait assessment and who can get it is large.

## Slide 3: Meet KneeGait-Edge
THE PROTOTYPE
A wearable edge-AI prototype that tracks shank motion during walking with a single IMU strapped to the shin.
Mounted on the flat anteromedial tibia to limit soft-tissue wobble.
From body movement to real-time gait intelligence.
01 SENSE
Shank IMU captures movement
02 COMPUTE
ESP32 processes in real time
03 ANALYZE
Gait features are extracted
04 VISUALIZE
BLE streams to the browser
Notes: Four stages: sense with the shank IMU, compute on the ESP32, analyze gait features, visualize in the browser over Web Bluetooth. Everything except the dashboard runs on the wearable.

## Slide 4: From Motion to Gait Intelligence
SYSTEM FLOW
SHANK IMU
ESP32
SENSOR FUSION
STRIDE FEATURES
RANDOM FOREST
BLE DASHBOARD
RESEARCH BACKED
Bytyqi et al. (2014)
Clinical thresholds
Peak swing flexion ≈ 41.9° in medial knee OA vs ≈ 58° in healthy controls; basis for the < 45° screening flag.
Rhudy et al. (2024)
Sensor fusion
Magnetometer-free complementary filter (α = 0.96 at 50 Hz); reported joint-angle RMSE ≤ 3.2° vs motion capture.
Song & Baxter (2025)
Placement & validation
Tibia-mounted IMUs limit soft-tissue artifact; reported Rxy ≥ 0.90 against optical motion capture.
Literature figures come from knee-angle studies, not from this prototype's own measurements.
Notes: The design choices trace back to three papers: Bytyqi for the clinical stiff-gait threshold, Rhudy for the complementary filter, Song and Baxter for tibial mounting. These are literature results, not our own validation.

## Slide 5: Simple Hardware. Smart Processing.
HARDWARE
ESP32 NodeMCU
Processing + BLE
1 × MPU-6050
6-axis motion sensing on the shank
USB power bank
Portable power
Elastic bandage
Wearable mounting
I²C BUS
SDA → GPIO 21 SCL → GPIO 22 Shank IMU → 0x68 (AD0 low) / 0x69 (AD0 high)
Cost democratization: capable sensing from components anyone can buy.
₹516 prototype cost
Notes: Four cheap parts. The MPU-6050 is on I2C (SDA GPIO 21, SCL GPIO 22). The address is 0x68 or 0x69 depending on the AD0 pin. The ₹516 figure is the out-of-pocket cost of this prototype.

## Slide 6: Turning Raw Motion Into Shank Angle
SIGNAL FUSION
1
ACCELEROMETER TILT
Inclination from gravity: atan2(−ax, √(ay²+az²))
2
GYROSCOPE INTEGRATION
Rotation over time: θ(t−Δt) + ω·Δt
3
COMPLEMENTARY FILTER
Fused angle with less noise and drift
θ(t) = 0.96 × [θ(t−Δt) + ω·Δt] + 0.04 × θacc(t)
50 Hz sampling • Δt = 20 ms • α = 0.96
One IMU gives shank inclination θshank, a proxy for knee motion. True knee flexion, |θthigh − θshank|, needs a second (thigh) sensor, which is planned next.
Notes: A complementary filter blends the gyroscope (smooth but drifts) with accelerometer tilt (noisy but drift-free). With 96% weight on the gyro path at 50 Hz it is cheap enough for the ESP32. With one shank sensor the output is shank angle, not knee flexion.

## Slide 7: From Strides to Features
GAIT ANALYSIS
HEEL-STRIKE EVENT DETECTION
≥ 1.45 g
Shank impact spike marks a heel strike
0.40 s
Refractory window rejects bounce and chatter
0.55–2.40 s
Valid stride duration (physiological bounds)
FIVE GAIT FEATURES PER STRIDE
1
Peak swing angle
Max shank angle during the swing phase
2
Sagittal range of motion
Max − min angle across the stride
3
Stance / swing ratio
Weight-bearing time ÷ swing time
4
Peak angular velocity
Max rate of rotation, max |dθ/dt|
5
Cadence
Steps per minute = 120 ÷ stride time (s)
Notes: Strides are cut at heel strikes, detected from the shank acceleration spike. Each stride yields five features that feed the classifier.

## Slide 8: Intelligence at the Edge
EDGE AI
RAW 50 Hz SHANK DATA
STRIDE SEGMENTATION
5 GAIT FEATURES
RANDOM FOREST (20 TREES, DEPTH 5)
ON-DEVICE INFERENCE (< 50 µs)
3-CLASS RISK OUTPUT
Normal gait
Peak swing flexion ≥ 49.4° · continue monitoring
Mild functional restriction
45.0° ≤ peak swing flexion < 49.4° · follow up
Severe antalgic stiff gait
Peak swing flexion < 45.0° · physician review
Random Forest → portable C header → ESP32 inference. No cloud needed for core inference.
Trained on 20,000 synthetic strides; thresholds are knee-flexion references. Validation on real gait data is a next step.
Notes: The classifier is a small random forest exported as a C header, so inference runs on the ESP32 in microseconds with no cloud. Important caveat: the training data is synthetic, and the class thresholds come from knee-flexion literature, so real-data validation is required.

## Slide 9: See the Gait in Real Time
LIVE EXPERIENCE
Chart: Live shank angle over time (illustrative)
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19
Shank angle (°) | 5 | 19 | 30 | 35 | 37 | 39 | 34 | 20 | 4 | -3 | 5 | 19 | 30 | 35 | 37 | 39 | 34 | 20 | 4 | -3
Web Bluetooth
Runs in Chrome or Edge, no app install
Risk badge
Green / amber / red triage at a glance
Reports
Session analytics, CSV export, printable PDF
Illustrative waveform; not patient data.
Notes: The dashboard talks to the ESP32 over Web Bluetooth, so there is no backend or app to install. The waveform shown is illustrative.

## Slide 10: From Movement to Meaning
BIOMECHANICAL CONTEXT
≈ 58°
Healthy mean peak swing flexion (Bytyqi 2014)
41.9°
Mean in moderate-to-severe medial knee OA
< 45°
Screening flag for stiff-gait risk, not a diagnosis
GAIT CYCLE
1 STANCE
2 TOE-OFF
3 MID-SWING
4 HEEL STRIKE
Research / hackathon prototype, not intended for medical diagnosis. Shank-only angles are a proxy for knee flexion, so thresholds need recalibration on real data.
Notes: Patients with knee OA tend to stiffen the knee during swing, reducing peak flexion. The < 45° line is a screening indicator from the literature, not a diagnosis, and our shank-only angle is a proxy that needs recalibration.

## Slide 11: From Prototype to Scalable Gait AI
ROADMAP
NOW
₹516 prototype
Single shank IMU
ESP32 edge AI
BLE web dashboard
NEXT
Add thigh IMU for true knee flexion
Real gait data and model validation
Compare with optical capture
Improved enclosure
FUTURE
Clinical validation
Bilateral left/right nodes
Insole force sensors
Cloud / EHR telehealth
POTENTIAL APPLICATIONS
Research • Physiotherapy support • Gait screening • Remote monitoring • Resource-constrained settings
Notes: Next step with the biggest impact: add the thigh IMU so the device measures true knee flexion and the literature thresholds apply directly, then collect real gait data to replace the synthetic training set.

## Slide 12: References & Acknowledgements
CREDITS
RESEARCH REFERENCES
Bytyqi, D., Shabani, B., Lustig, S., Cheze, L., Gjurgjeala, N. K., & Neyret, P. (2014). Gait knee kinematic alterations in medial osteoarthritis: Three-dimensional assessment. International Orthopaedics, 38(6), 1191–1198. https://doi.org/10.1007/s00264-014-2312-3
Rhudy, M. B., Mahoney, J. M., & Altman-Singles, A. R. (2024). Knee angle estimation with dynamic calibration using inertial measurement units for running. Sensors, 24(2), 695. https://doi.org/10.3390/s24020695
Song, K., & Baxter, J. R. (2025). Body-worn inertial measurement units track knee flexion angles with similar accuracy to optical motion capture. medRxiv. https://doi.org/10.1101/2025.10.20.25338317
Espressif Systems. (2023). ESP32 Low-Power Management and RF Power Consumption Specification. Espressif Architecture Documentation, Rev. 3.4.
Note: this is a hackathon/research prototype. Dashboard values shown are illustrative, not patient results.
Democratizing Gait Intelligence.
Notes: Reiterate the prototype status and that dashboard values are illustrative.